5946 Millbury Court

Charlotte NC 28211

EMail: galden@pooldesignconsultants.com 		Telephone 704/362-3144

### Web Site at www.pooldesignconsultants.com

City Lake Park Renovation, City of High Point, NC

- This work was done through Alden Enterprises Inc. prior to Pool Design Consultants, Inc. being formed.

- EXISTING CONDITIONS: The pool is in the shape of a Eastern Orthodox Cross with a 25 yd x 6 lanes making up one size, a zero entry at the bottom and a curved step down area at the top.

- SCOPE OF WORK:

  - Demolition of the pool equipment and piping in the pool equipment room and the pipe chase that circumscribed the pool.

  - The concrete gutter was renovated with a new grating system installed

  - Construction of a code compliant chemical storage room

  - Design and provide a filter that would be able to be lowered into an equipment room shown in the pictures.

  - Provide dual pump system with rotating on/off abilities

  - Provide an automatic chemical feed controller with chlorine and CO2 feed

  - Provide an automatic water level controller

  - Provide updated piping layout using Schedule 80 Type 1 PVC and either flanged butterfly valves or true union ball valves

  - Provide training and operational information for staff operations

  - Provide support for the systems for one year.

- The installation work was provided by a Meredith Pools of Greenboro NC and was completed on time to be opened for the 1992 summer season.